## Slide 1: Error Budgeting for Superconducting Modular Quantum Architecture Designs
APS March Meeting (2025)

## Slide 2: Transpilation as co-design framework
Circuit mapping
Control optimization
Device execution
Gate decomposition to ISA
Quantum algorithm
  How much qubit connectivity is feasible with high fidelity?
Gate fidelity threshold
# qubits per module
qubit-coupler connectivity
Qubit frequency allocation
# unique qubit frequencies
Device Constraints
mode frequency bandwidth
fabrication precision
hybridization strengths
coupler speed-limit
Connectivity reduces circuit costs
McKinney, et al. HPCA (2023)
Notes:   Maximum vertex variants?
  Maximum incident edges per node?
  Maximum adjacent vertices?

## Slide 3: Four qubit SNAIL-based quantum module
Xia, et al. arXiv:2306.10162 (2023)
Zhou, et al. npj Quantum Inf 9, 54 (2023)
Frattini, et al. Applied Physics Letters (2017)
SNAIL (coupler)
Transmon (qubit)
Module:
Yusuf, MAR-A18.13
Repicky, MAR-L18.13
SNAIL:
Wang, MAR-W09.11
Mesits, MAR-N17.3
Nowicki, MAR-T09.11

## Slide 4: Gate crowding in a module
de Freitas, et al. ITOR (2021)
Park, et al. J. Oper. Res. Soc. Jpn. (1996)
Pairs of driven interactions
Edge: conversion frequency
“Compatibility graph”
Edge: separation constraint (q)
Memarsadeghi. CSE (2016)
Frequency Allocation Problem
Notes: Classically, this is a linear constraint optimization problem (Frequency Allocation Problem)!
Edges in compatibility graph specify a minimum separation constraint

## Slide 5: Spectral crowding of terms
Zhou, Chao. PhD Thesis (2023)
Notes: Diagonalization, pump displacement transforms to get an interaction frame Hamiltonian.
Then we do the polynomial expansions to get full set of terms.
See that the e^-iwt terms give the pump frequencies, such that these terms go to 1 (or 0 otherwise). But when crowded, this breaks down.
Call these spectator terms, inherent crowding sources due to inadvertently activating more than the desired term due to features of the spectral allocation

## Slide 6: Sources of infidelity from module crowding
Incoherent loss from speed limits
Unwanted unitary terms decay with detuning
Coherent error from spectators
Experimentally characterized max drive strength
Remove explicit time-dependence with a worst-case approximation.
Zhou, Chao. PhD Thesis (2023)
McKinney, et al. ISCA (2023)
Parametric Speed limits: Xia, MAR-L36.2 Capocci, MAR-L36.3
Notes: Plug other MM talks, Jake/Mingkang/Blais;

## Slide 7: Error budgeting against spectators
For each interaction, use infidelity vs detuning characterization in Nelder-Mead minimization to allocate best mode frequencies
Notes: Walk through graph carefully how do you get out of it, either make the gates slower or make detuning larger!!!

## Slide 8: Module fidelities from optimized frequency stacks
N-qubit module | Avg gate fidelity
2 | .996
3 | .994
4 | .990
5 | .940
Notes: Need to emphasize the key ingredients
Assume lifetime, assume speed limit – put numbers on the slide!

## Slide 9: Tradeoffs between gate speed and spectators
Larger frequency bandwidth: increase spectator detunings
Longer qubit lifetimes: slower gates, weaker spectators
Wei, et al. Phys Rev Applied (2024)
Threshold at
Notes: Assume lifetime, assume speed limit – put numbers on the slide!
Turn up the T1 by 10 and reoptimize with new spectators

## Slide 10: Conclusions
Developed a fidelity model from characterized device properties
  Quantified tradeoffs between coherent and incoherent noise sources
  Develop numerical optimization to minimize total average gate infidelity
Frequency allocation problem to determine viable module sizes
  SNAIL module supports up to 4 qubits before fidelity drops below 0.99
  Partial frequency allocation improves base fidelity up to 0.994, yielding a 19.9% relative improvement in computational accuracy.
Alex K. Jones
Girgis Falstin
Israa Yusuf
Gaurav Agarwal
Michael Hatridge
SNAIL
Qubit
Up next: Yusuf, MAR-A18.13
McKinney, et al. arXiv:2409.18262 (2024)

## Slide 11: Procedurally generating topologies
1: Satisfy all edges from input
2: Add nodes to until saturate all couplers
3: Verify isomorphism between input output
Selective edge removal
Sacrificing dense connectivity for less spectator crowding is a worthwhile tradeoff!
Greedy inverse bipartite projection
Notes: 205 valid bipartite graph using 4-8 SNAILs with at least 16 qubits. (using constraint of 2-colorable module graph, max degree of snail 4, max degree of qubit 2)